Mel scale

The mel scale, named by Stevens, Volkman and Newman in 1937[1] is a perceptual scale of pitchesjudged by listeners to be equal in distance from one another. The reference point between this scale and normal frequency measurement is defined by assigning a perceptual pitch of 1000 mels to a 1000 Hz tone, 40 dB above the listener's threshold. Above about 500 Hz, larger and larger intervals are judged by listeners to produce equal pitch increments. As a result, four octaves on the hertz scale above 500 Hz are judged to comprise about two octaves on the mel scale. The name mel comes from the word melody to indicate that the scale is based on pitch comparisons.
A popular formula to convert f hertz into m mel is:

Converting frequency domain to mel frequency

Use triangular overlapping windows defined as:

Cepstrum

A cepstrum /ˈkɛpstrəm/ is the result of taking the Inverse Fourier transform (IFT) of the logarithm of the estimated spectrum of a signal.
The power cepstrum was defined in a 1963 paper by Bogert et al.[1] The power cepstrum of a signal is defined as the squared magnitude of the inverse Fourier transform of the logarithm of the squared magnitude of the Fourier transform of a signal.[2]
power cepstrum of signal
The independent variable of a cepstral graph is called the quefrency. The quefrency is a measure of time, though not in the sense of a signal in the time domain. For example, if the sampling rate of an audio signal is 44100 Hz and there is a large peak in the cepstrum whose quefrency is 100 samples, the peak indicates the presence of a pitch that is 44100/100 = 441 Hz. This peak occurs in the cepstrum because the harmonics in the spectrum are periodic, and the period corresponds to the pitch. Note that a pure sine wave should not be used to test the cepstrum for its pitch determination from quefrency as a pure sine wave does not contain any harmonics. Rather, a test signal containing harmonics should be used (such as the sum of at least two sines where the second sine is some harmonic (multiple) of the first sine).

1. EM algorithm
2. Multivariate gaussian density
3. Sphinx?
4. Graphemes, phonemes, senomes?
5. Algorithms descriptions
6. Tests descriptions

Experiments:
  - length based sentences alignment
  - russian audio model word alignment
  - russian audio model phoneme alignment
  - trained polish simplified audio model phoneme alignment