Abstract

The purpose of this final master degree project was to experiment with various algorithms for speech and text alignment either with granularity of sentences, single words or even single phonemes. The output of this study was expected to find out how little data is necessary to give a proper alignment at various levels. This project focuses mainly on polish language, however it can be quite easily generalized for different languages. From so many different dialects in the world one can always find similar, like I did with polish and russian. I also focus solely on a audio with quite low level of noise, since noise introduces a lot of problems, which are out of the scope of this project.

Contents

1. Introduction
2. Speech signal
  1. Human factor
  2. Mel scale.
  3. Frequency spectrum.
  4. Mel-spectrum.
  5. Cepstrum
  6. Sphinx frontend
3. Speech modelling
  1. Phonetics
  2. Audio distances
  3. Phoneme gaussian models
  4. Hidden Markov Model
  5. EM algorithm
  6. Baum-Welch algorithm
4. Simple pause and length alignment.
  1. Speech detection
  2. Length alignment
5. Word alignement based on similar audio model.
  1. Speech recognition.
  2. Differences between Russian, Polish and English phonology.
  3. Grapheme to phoneme conversion grammar.
  4. Alignement using audio model.
6. Phoneme alignment.
  1. Introduction
  2. Approaches
  3. Test results
7. Training audio from large audio files
  1. Putting all together
  2. Test results
8. Testing alignement with synthesizer.
  1. Introduction
  2. Approach
  3. Test results
9. Summary and conclusion.
10. Bibliography

1. Introduction

2. Speech Signal

  1. Human factor

Speech is a most efficient way the human communicate. For generations this process was refined by evolution, so we can easily exchange messages even in hard situations. For this purpose our vacal mechanisms must well cooperate with our hearing ability. There is a certain set of sounds we can produce, so our ears evolved to hear them as well as possible.

What is sound? According to dictionary: „Vibrations transmitted through an elastic solid or liquid or gas, with frequencies in the approximate range of 20 to 20000 hertz, capable of being detected by human organs of hearing”. [1]

How do we hear? Human ear consist about 30000 hair-cells, which can convert mechanical wave of the sound into electromagnetic wave inside auditory nerves [2].
Each of these cell is excited by different frequency of mechanical wave of internal ear fluids, so it is no suprise, that people can hear only a certain range of frequencies, as stated in definition. These we expect to be finely tuned to the frequencies of the sounds we can produce. Although it seems, that we can hear a bit more, but as we don't need them it happens, that as we grow older our hearing range is getting smaller, because our hear cells fail sometimes, but mostly those responisble for high requencies, which we don't use too often.

Humans can hear frequencies, that begins as low as 12Hz (under laboratory conditions) to 20kHz (for adults usually much lower). However speech range is a little bit smaller than that [3]:

  2.2. Mel scale.
How we perceive sound, that is completely different matter and topic for long phylosophical discussion. However we can help ourselves we some subjective experiments. For example Stevens, Volkman and Newman conducted an experiment on a number of listeners to measure, what do we perceive as equaly distanced pitches. In this experiment, the participants of the experiment were asked to judge if given pitches were subjectively in equal distances. The output was, that humans don't experience sound linearly to the frequency scale, but a perceptual scale was closer to logarithmic one. [5]

Certain formulas were conceived to translate frequency scale to some, that is closer to how human actually perceive sound.

One popular is mel scale, where mel comes from melody: [6]
m = 2595log_{10}(1 + f over {700})
  What looks like that:

Another popular formula of so called bark scale, which is based on perception of loudness of the sound and proposed by Eberhard Zwicker in 1961. [7]
Bark = 13 atan({0.76f} over {1000}) + 3.5 atan({f^2} over {7500^2})

In this project we use mel scale implemented in sphinx library, although bark scale is becoming more popular recently.

  2.2. Frequency spectrum.

The conclusion from the anatomy of human ear is, that frequencies of the sound are important.
How can we obtain frequency spectrum from a digitilized sound, so we can process this further?

The obvious tool for conversion of discrete function to frequencies is Discrete Fourier Transform.
Named after Jean Baptiste Joseph Fourier it is one of the most often used techniques of modern times.

It all starts from the postulate, that a heat equation can be satisfied by function of form: [11]
f(x)=sum_{n=0}^N(A_n cos(nx) + B_n sin(nx))
or in complex form:
f(%iteta)=sum_{n=-infinity}^{infinity} C_n e^{i n %iteta}
Basically we convert our function's domain to frequency domain or to domain of sinusoidal functions. C_n coefficients are complex values that encode bother amplitude and phase of the converted signal/function at each frequency.

The coefficients for any integrable functions over an interval [-T over 2 , T over 2] can be obtain using formula: [11]
C_n=int_{-T over 2}^{T over 2} f(x) e^{-2 %ipi i n over T x} dx
or for the discrete case:
C_k=sum_{n=0}^{N-1} x_n e^{-2 %ipi i k n / N} dx

So far we haven't found any use in the speech recognition for phase part of the coefficients, however amplitude determins how powerful is signal at given frequncy. The power value is given by:
lline X_k rline / N = sqrt(Re(X_k)^2 + Im(X_k)^2) / N
A sample conversion:

What size of the window should we use? First we have to notice, that in order to capture certain frequency, the window needs to be large enough. We would like to examine signals of frequency ranged from 100Hz (see speech frequncies ranges in chapter 2.1), which is a period of 100th of the second so a 10millisecond window would be our bottom limit.

Also windows with abrupt signal discontinuities may cause result with spectral artifacts, so a windowing function is usually applied. Popular choice is a Hamming window function: [8]
w_j = 0.54 - 0.46 cos({2 %ipi j} over {W - 1})
Which's plot is:

Note that it emphasises values in the middle of the window, so our actual windows should overlap to cover whole time domain. For example by shifting a window by a percentage of it actual width:

A human speech signal in frequency and time domain: [3]

  2.3. Mel-freq spectrum.

Mel scale is created using triangular overlapping windows.

  The problem with frequency analysis, is that it contains a lot of data points even for limited range of frequencies and fast online or even reasonable offline analysis it quickly becomes infisible.
  Converting frequency domain to mel frequency
3. Use triangular overlapping windows defined as:

  2.2. Cepstrum.
  Looking at the frequency spectrum of human speech we see, that the singal in the frequency domain contain features that are quite periodic.
We often use a power sp

MFCCs are commonly derived as follows:[1][2]
1. Take the Fourier transform of (a windowed excerpt of) a signal.
2. Map the powers of the spectrum obtained above onto the mel scale, using triangular overlapping windows.
3. Take the logs of the powers at each of the mel frequencies.
4. Take the discrete cosine transform of the list of mel log powers, as if it were a signal.
5. The MFCCs are the amplitudes of the resulting spectrum.

A cepstrum /ˈkɛpstrəm/ is the result of taking the Inverse Fourier transform (IFT) of the logarithm of the estimated spectrum of a signal.
The power cepstrum was defined in a 1963 paper by Bogert et al.[1] The power cepstrum of a signal is defined as the squared magnitude of the inverse Fourier transform of the logarithm of the squared magnitude of the Fourier transform of a signal.[2]
power cepstrum of signal
The independent variable of a cepstral graph is called the quefrency. The quefrency is a measure of time, though not in the sense of a signal in the time domain. For example, if the sampling rate of an audio signal is 44100 Hz and there is a large peak in the cepstrum whose quefrency is 100 samples, the peak indicates the presence of a pitch that is 44100/100 = 441 Hz. This peak occurs in the cepstrum because the harmonics in the spectrum are periodic, and the period corresponds to the pitch. Note that a pure sine wave should not be used to test the cepstrum for its pitch determination from quefrency as a pure sine wave does not contain any harmonics. Rather, a test signal containing harmonics should be used (such as the sum of at least two sines where the second sine is some harmonic (multiple) of the first sine).

  1. Sphinx frontend.

Sphinx is a speech recognition toolkit with a lot of useful features for any speech related problem.
There is a certain common way to prepare a speech signal for the further processing. With slight variations in each step, the useful informations about speech are drawn from a cepstrum of the reduced signal (in the number of data dimensions), as presented in this chapter.

In order to skip the reinventing the wheel, I used the fronted part of the sphinx library for any experiment in this project. The sphinx fronted performs signal transformation and produces data composed of only 39 voice features, while actually only 13 are base ones and the rest is a derivation of these.

Sphinx frontend is a list of transformations executed on the result of the transformation placed higher in the list or stated differently a transformation composition.
This includes:
Data Blocker,
Preemphasizer,
Windower,
Discrete Fourier Transform,
Mel Frequency Filter Bank,
Discrete Cosine Transform,
Live CMN,
Deltas Feature Extractor.

    1. Data Blocker

This initial transformation reads incoming double data read from audio source (wav or microphone) and
prepares blocks of the data to be used in later phases. In our case blocks contain 10ms of audio data.

    1. Preemphasizer

The Preemphasizer applies a formula: Y[i]=x[i]-(X[i-1] * preemphasizerFactor) .
The purpose of this transformation is to emphasize the high frequency components. It is kind of filter,
which allows high frequency components to pass through, but weakens the low frequency ones.

    1. Raised cosine windower

Creates windows from the incoming data. A windowing function W(n)=(1-%ialfa) - %ialfa cos({2 %ipi n} over {N - 1})
 is applied afterwards. Alpha coefficient set to 0.46 gives a mentioned before Hamming windowing
 function, which is a default setting and the one used by me.

    1. Discrete Fourier Transform

Implementation of fast fourier transform .The FFT can perform this operation in %iOMEGA(Nlog(N)) which is fast enough for small enough windows.

    1. Mel frquency filter bank

Conversion of frequency spectrum into a mel-spectrum filter banks.

Typical values for the constants defining the filter bank are:
Sample rate (Hz)	16000	11025	8000
numberFilters	40	36	31
minimumFrequency(Hz)	130	130	200
maximumFrequency(Hz)	6800	5400	3500

Davis and Mermelstein showed that Mel-frequency cepstral coefficients present robust

Filters an input power spectrum through a bank of number of mel-filters. The output is an array of filtered values, typically called mel-spectrum, each corresponding to the result of filtering the input spectrum through an individual filter. Therefore, the length of the output array is equal to the number of filters created.
The triangular mel-filters in the filter bank are placed in the frequency axis so that each filter's center frequency follows the mel scale, in such a way that the filter bank mimics the critical band, which represents different perceptual effect at different frequency bands. Additionally, the edges are placed so that they coincide with the center frequencies in adjacent filters. Pictorially, the filter bank looks like:

Figure 1: A Mel-filter bank.
As you might notice in the above figure, the distance at the base from the center to the left edge is different from the center to the right edge. Since the center frequencies follow the mel-frequency scale, which is a non-linear scale that models the non-linear human hearing behavior, the mel filter bank corresponds to a warping of the frequency axis. As can be inferred from the figure, filtering with the mel scale emphasizes the lower frequencies. A common model for the relation between frequencies in mel and linear scales is as follows:
melFrequency = 2595 * log(1 + linearFrequency/700)
The constants that define the filterbank are the number of filters, the minimum frequency, and the maximum frequency. The minimum and maximum frequencies determine the frequency range spanned by the filterbank. These frequencies depend on the channel and the sampling frequency that you are using. For telephone speech, since the telephone channel corresponds to a bandpass filter with cutoff frequencies of around 300Hz and 3700Hz, using limits wider than these would waste bandwidth. For clean speech, the minimum frequency should be higher than about 100Hz, since there is no speech information below it. Furthermore, by setting the minimum frequency above 50/60Hz, we get rid of the hum resulting from the AC power, if present.
The maximum frequency has to be lower than the Nyquist frequency, that is, half the sampling rate. Furthermore, there is not much information above 6800Hz that can be used for improving separation between models. Particularly for very noisy channels, maximum frequency of around 5000Hz may help cut off the noise.
Typical values for the constants defining the filter bank are:
Sample rate (Hz)	16000	11025	8000
numberFilters	40	36	31
minimumFrequency(Hz)	130	130	200
maximumFrequency(Hz)	6800	5400	3500

Davis and Mermelstein showed that Mel-frequency cepstral coefficients present robust characteristics that are good for speech recognition. For details, see Davis and Mermelstein, Comparison of Parametric Representations for Monosyllable Word Recognition in Continuously Spoken Sentences, IEEE Transactions on Acoustic, Speech and Signal Processing, 1980 .

    1. Discrete Cosine Transform

Applies a logarithm and then a Discrete Cosine Transform (DCT) to the input data. The input data is normally the mel spectrum. It has been proven that, for a sequence of real numbers, the discrete cosine transform is equivalent to the discrete Fourier transform. Therefore, this class corresponds to the last stage of converting a signal to cepstra, defined as the inverse Fourier transform of the logarithm of the Fourier transform of a signal. The propertyPROP_CEPSTRUM_LENGTHrefers to the dimensionality of the coefficients that are actually returned, defaulting to 13. When the input is mel-spectrum, the vector returned is the MFCC (Mel-Frequency Cepstral Coefficient) vector, where the 0-th element is the energy value.

In particular, a DCT is a Fourier-related transform similar to the discrete Fourier transform (DFT), but using only real numbers. DCTs are equivalent to DFTs of roughly twice the length, operating on real data with even symmetry (since the Fourier transform of a real and even function is real and even), where in some variants the input and/or output data are shifted by half a sample. There are eight standard DCT variants, of which four are common.

Formally, the discrete cosine transform is a linear, invertible function  (where  denotes the set of real numbers), or equivalently an invertible N× N square matrix. There are several variants of the DCT with slightly modified definitions. The N real numbers x0, ..., xN-1 are transformed into the N real numbersX0, ..., XN-1 according to one of the formulas:
### DCT-I[edit]

    1. Live Cepstral Mean Normalization

Subtracts the mean of all the input so far from the Data objects. Unlike the BatchCMN, it does not read in the entire stream of Data objects before it calculates the mean. It estimates the mean from already seen data and subtracts the mean from the Data objects on the fly. Therefore, there is no delay introduced by LiveCMN.
The Sphinx properties that affect this processor are defined by the fields PROP_INITIAL_MEAN, PROP_CMN_WINDOW, and PROP_CMN_SHIFT_WINDOW. Please follow the link "Constant Field Values" below to see the actual name of the Sphinx properties.
The mean of all the input cepstrum so far is not reestimated for each cepstrum. This mean is recalculated after every PROP_CMN_SHIFT_WINDOW cepstra. This mean is estimated by dividing the sum of all input cepstrum so far. After obtaining the mean, the sum is exponentially decayed by multiplying it by the ratio:
 cmnWindow/(cmnWindow + number of frames since the last recalculation)

This is a 1-to-1 processor.

    1. Deltas feature extractor

Computes the delta and double delta of input cepstrum (or plp or ...). The delta is the first order derivative and the double delta (a.k.a. delta delta) is the second order derivative of the original cepstrum. They help model the speech signal dynamics. The output data is a FloatData object with a float array of size three times the original cepstrum, formed by the concatenation of cepstra, delta cepstra, and double delta cepstra. The output is the feature vector used by the decoder. Figure 1 shows the arrangement of the output feature data array:

Figure 1: Layout of the returned features.
Suppose that the original cepstrum has a length of N, the first N elements of the feature are just the original cepstrum, the second N elements are the delta of the cepstrum, and the last N elements are the double delta of the cepstrum.
Figure 2 below shows pictorially the computation of the delta and double delta of a cepstrum vector, using the last 3 cepstra and the next 3 cepstra.
Figure 2: Delta and double delta vector computation.
Referring to Figure 2, the delta is computed by subtracting the cepstrum that is two frames behind of the current cepstrum from the cepstrum that is two frames ahead of the current cepstrum. The computation of the double delta is similar. It is computed by subtracting the delta cepstrum one time frame behind from the delta cepstrum one time frame ahead. Replacing delta cepstra with cepstra, this works out to a formula involving the cepstra that are one and three behind and after the current cepstrum.

3. Speech Modelling.

  1. Phones and phonemes.

Language grapheme sets usually differs quite substantially from it audio counterparts.
Usually it contains more characters than needed to represent every word from given language and at the same time it is much to smaller to represent all the nuances of human speech. What is more problematic, the word graphic represantation often has very little to do with actual phonemes of the same word. There are multiple words, that are written the same yet it pronunciation differs or the other way round, when it looks differently, but is pronunced the same or very similar.

For each language a study is performed concerned with the systematic organization of sounds in it.
This branch of linquistics called phonology comes up with a system of phonetic alphabet which, can describe how each word should be spoken. Computational phonology often uses this system to train recognition software for each phoneme separately.

Phoneme: the basic theoretical unit for describing how speech conveys linguistic meaning.
In English, there are about 42 phonemes.
an ideal sound unit with a complete set of articulatory gestures.

Types of phonemes: vowels, semivowels, dipthongs, and consonants.

Phone: the actual sounds that are produced in speaking (for example, "d" in letter pronounced "l e d er").
Phonetics: the study of the actual sounds of the language
Allophones: the collection of all minor variants of a given sound ("t" in eight versus "t" in "top")

Monophones, Biphones, Triphones: sequences of one, two, and three phones. Most often used to describe acoustic models.

  1. Audio distances.

The simplest way of searching of similar audio sequence is to find an audio sequence which is nearby to some, that we know represents a certain sound, phoneme or word.

The Euclidean distance measure is the ”standard” distance measure between
two vectors in feature space (with dimension DIM ) as you know it from school:
        d^{2}_{Euclid} = sum csub{i = 0} csup{DIM - 1} (x_{i} - p_{i})^2
To calculate the Euclidean distance measure, you have to compute the sum of
the squares of the differences between the individual components of x and p.
This can also be written as the following scalar product:

        d^{2}_{Euclid}(vec x, vec p) = (vec x - vec p)' cdot (vec x - vec p)

where ′ denotes the vector transpose. Note that both equations (3.1) and (3.2)
compute the square of the Euclidean distance, d2 instead of d. The Euclid-
ean distance is probably the most commonly used distance measure in pattern
recognition.

So far, we can deal with different scales of our features using the weighted
Euclidean distance measure. This works very well if there is no correlation
between the individual features as it would be the case if the features we selected
for our vector space were statistically independent from each other. What if
they are not? Figure 3.2 shows an example in which the features x1 and x2 are
correlated.
Obviously, for both classes A and B, a high value of x1 correlates with a high
value for x2 (with respect to the mean vector (center) of the class), which is
indicated by the orientation of the two ellipses. In this case, we would want
the distance measure to regard both the correlation and scale properties of the
features. Here a simple scale transformation as in (3.4) will not be sufficient.
Instead, the correlations between the individual components of the feature vec-
tor will have to be regarded when computing the distance between two vectors.
This leads us to a new distance measure, the so–called Mahalanobis Distance:

d_Mahalanobis(vec x, vec p, tilde C) = (vec x - vec p) cdot {tilde C}^{-1} cdot (vec x - vec p)

Where tilde C denotes a covariance matrix.

If we knew elements belonging to given phoneme, we could calculate a distance from a phoneme.

  1. Gaussian Model.

#### Non-degenerate case[edit]
The multivariate normal distribution is said to be "non-degenerate" when the symmetric covariance matrix  %iSIGMA  is positive definite. In this case the distribution has density:
f_x(x_1,...,x_k) = {1}over{sqrt{(2%ipi)^2 lline {%iSIGMA} rline }}exp(-{1}over{2}(x-%imi )^T{%iSIGMA}^{-1}(x-%imi))

where  left lline %iSIGMA right rline  is the determinant of  %iSIGMA . Note how the equation above reduces to that of the univariate normal distribution if  %iSIGMA  is a 1x2 matrix (i.e. a real number).
Each iso-density locus—the locus of points in k-dimensional space each of which gives the same particular value of the density—is an ellipse or its higher-dimensional generalization; hence the multivariate normal is a special case of the elliptical distributions.

A log likelihood function for a single observation x would be:

ln(L) = {1}over{2}ln((2%ipi)^2 lline {%iSIGMA} rline) - {1}over{2}(x-%imi )^T{%iSIGMA}^{-1}(x-%imi)

If we had data belonging to a single phone, we could calculate normal distribution and use it to calculate for any given point a probability or log likelihood of belonging to the given class.

  1. Gaussian Mixture Model

In statistics, a mixture model is a probabilistic model for representing the presence of subpopulations within an overall population, without requiring that an observed data-set should identify the sub-population to which an individual observation belongs. Formally a mixture model corresponds to the mixture distributionthat represents the probability distribution of observations in the overall population. However, while problems associated with "mixture distributions" relate to deriving the properties of the overall population from those of the sub-populations, "mixture models" are used to make statistical inferences about the properties of the sub-populations given only observations on the pooled population, without sub-population-identity information.

  1. EM algorithm

### Expectation maximization (EM)[edit]
Expectation maximization (EM) is seemingly the most popular technique used to determine the parameters of a mixture with an a priori given number of components. This is a particular way of implementing maximum likelihood estimation for this problem. EM is of particular appeal for finite normal mixtures where closed-form expressions are possible such as in the following iterative algorithm by Dempster et al. (1977)

with the posterior probabilities

Thus on the basis of the current estimate for the parameters, the conditional probability for a given observation x(t) being generated from state s is determined for each t = 1, …, N ; N being the sample size. The parameters are then updated such that the new component weights correspond to the average conditional probability and each component mean and covariance is the component specific weighted average of the mean and covariance of the entire sample.
Dempster[7] also showed that each successive EM iteration will not decrease the likelihood, a property not shared by other gradient based maximization techniques. Moreover EM naturally embeds within it constraints on the probability vector, and for sufficiently large sample sizes positive definiteness of the covariance iterates. This is a key advantage since explicitly constrained methods incur extra computational costs to check and maintain appropriate values. Theoretically EM is a first-order algorithm and as such converges slowly to a fixed-point solution. Redner and Walker (1984)[full citation needed] make this point arguing in favour of superlinear and second order Newton and quasi-Newton methods and reporting slow convergence in EM on the basis of their empirical tests. They do concede that convergence in likelihood was rapid even if convergence in the parameter values themselves was not. The relative merits of EM and other algorithms vis-à-vis convergence have been discussed in other literature.[8]
Other common objections to the use of EM are that it has a propensity to spuriously identify local maximisers,[9] as well as displaying sensitivity to initial values.[citation needed] One may address these problems by evaluating EM at several initial points in the parameter space but this is computationally costly and other approaches, such as the annealing EM method of Udea and Nakano (1998) (in which the initial components are essentially forced to overlap, providing a less heterogeneous basis for initial guesses), may be preferable.
Figueiredo and Jain [5] note that convergence to 'meaningless' parameter values obtained at the boundary (where regularity conditions breakdown, e.g., Ghosh and Sen (1985)) is frequently observed when the number of model components exceeds the optimal/true one. On this basis they suggest a unified approach to estimation and identification in which the initial n is chosen to greatly exceed the expected optimal value. Their optimization routine is constructed via a minimum message length (MML) criterion that effectively eliminates a candidate component if there is insufficient information to support it. In this way it is possible to systematize reductions in n and consider estimation and identification jointly.
The Expectation-maximization algorithm can be used to compute the parameters of a parametric mixture model distribution (the ai and θi). It is an iterative algorithm with two steps: an expectation step and a maximization step. Practical examples of EM and Mixture Modeling are included in the SOCRdemonstrations.
#### The expectation step[edit]
With initial guesses for the parameters of our mixture model, "partial membership" of each data point in each constituent distribution is computed by calculatingexpectation values for the membership variables of each data point. That is, for each data point xj and distribution Yi, the membership value yi, j is:

#### The maximization step[edit]
With expectation values in hand for group membership, plug-in estimates are recomputed for the distribution parameters.
The mixing coefficients ai are the means of the membership values over the N data points.

The component model parameters θi are also calculated by expectation maximization using data points xj that have been weighted using the membership values. For example, if θ is a mean μ

With new estimates for ai and the θi's, the expectation step is repeated to recompute new membership values. The entire procedure is repeated until model parameters converge.

  1. Hidden Markov Model

We can describe a HMM by a triple: λ = ( A, B, π ) , where A is a transition matrix A={aij}=p(Qt=j|Qt-1=i} , B is a observation probability function vector B={bi}, where each bi is a function, that calculates a probability that a given observation Qt is produced by state i, a π is initial state distribution πi=P(Q1=i)

For our purpose a B functions will be a guassian multivariate distribution of given state.

The most probably state sequence for given sequence of observation can be calculated using dynamic programming with an Viterbi algorithm.

Initialization, for all s ∈ X : δ1 (s) = πs Ms,z1
Pre1 (s) = null.
Repeat, for k = 1, . . . , t − 1, and for all s ∈ X :
δk+1 (s) = maxq (δk (q)Tq,s ) Ms,zk+1
Prek+1 (s) = arg maxq (δk (q)Tq,s )
Select most likely terminal state:
st = arg maxs δt (s)
Backtrack to find most likely path.
For k = t − 1, . . . , 1 qk = Prek+1 (qk+1 )
The joint probability of the most likely path + observations is found
as p ∗ = δt (st ).

  1. Baum Welch algorithm

For training Hidden Markov Models we have to use a generalized version of EM algorithm, namely Baum-Welch algorithm.

For HMM training we have observed data X and we want to find parameters set θ, which will maximized the proobability of observing X, meaning argmax_θ(Pr(X | θ)).
If we knew what was the sequence of states in the HMM, this would be problem, which we could calculate optimal value of θ parameters. However we don't know, what the states of HMM were, hence hidden in the name. On the other hand if we knew θ, then we would easily calculate sequence of states, which would maximize the probability using Viterbi algorithm.
EM algorithm is meant for such a situations.

In the EM spirit, for each iteration we will perform two steps, bringing us to some local maximum:
  - expectation step
Given previous estimation of parameters θ, we calculate the probability of being at any given time t at any states Pr(s_i, t)
  - maximization
Given probabilities of being at any state, we calculate next estimation of θ parameters, which will maximize the likelihood of observing X: argmax_θ(Pr(X | θ))

How can we calculate θ parameters?
Θ = {A, B}, where:
A – transition probabilities (probability of transition between any two states)
B – observation probabilities (probability of observing any data at any given time)

To calculate observation probabilities, we need:
α_i(t) = Pr(being after t steps at state i)

        β_i(t) = Pr(ending sequence mline being after t steps at state i)

Both of these values can be calculated using dynamic programming. One is calculated by Viterbi's algorithm in forward passage, the other can be calculated in similar manner by backward passage.

Combining these values, we can obtain:

Pr(size 10 {being at time} bold{t} size 10 {at state} bold{i}) = {α_i(t)β_i(t)} over {sum_{j=1}^{N} α_j(t)β_j(t) }

and:

Pr( size 10 {transition between states} bold{i} bold{j} size 10 {at time} bold{t}) = {α_i(t)a_{ij}β_j(t + 1)b_j(o_{t+1})} over {sum_{i=1}^{N} sum_{j=1}^{N} α_i(t)a_{ij}β_j(t + 1)b_j(o_{t+1})}

While probability of transition from states i to state j at any given time is:

Pr(transition i j) = {sum_{t=1}^{T-1} Pr( size 10 {transition between states} bold{i} bold{j} size 10 {at time} bold{t})} over {sum_{t=1}^{T-1} Pr(size 10 {being at time} bold{t} size 10 {at state} bold{i}) }

While just a probability of being at time t at state i can be used to calculated new probabilities of observing o_t (observation at time t) from given state, since it is emitted by state i with probability of being at this state at this time.

New parameters of multivariate normal distribution would look like:

vec %imi = 1 over T sum_{t=1}^{T} Pr(size 10 {being at time} bold{t} size 10 {at state} bold{i})vec o_t

tilde C = 1 over T sum_{t=1}^{T} Pr(size 10 {being at time} bold{t} size 10 {at state} bold{i})(vec o_t - vec %imi) cdot (vec o_t - vec %imi)^T

4. Simple pause and length based alignment

The basic idea behind this approach is to match sentences with continous sequence of speech.
Humans rarely make pauses inside a subsentence and rarely continue to another sentence without a pause.
One simple approach to the alignment problem which uses above fact is to try match part of speech with a text which would take a similar time to say it.

  1. Speech Detection

Before we can continue with alignement, we need to detect pauses first. This problem is exactly a problem of detecting speeches.

On its own in various enviroments this problem is quite hard, however we don't want to consider situations where extracting speech from background is too difficult. It is true, that humans are quite proficient at extracting speech from quite challanging situations like recognizing words of the song, are distinguishing speakers in a crowd.
However even humans are not perfect, and is often prone for errors. Recognizing song lyrics can be sometimes quite challenging, and it remains an open question how much you can attributes this to background music, how much to changed modulation of singer voice and how much to overabundance of signal in melody scale. On the other hand, humans can recognize voice in white noise.

We leave this problematic cases and focus only on situations where noise to signal ratio is low and we can utilize statistics to detect speech.

  1. Text to sentences split

Before we can continue with alignment, we still would like to have text split to sentences. It is necessary to have a certain knowledege about punctuation in given language. However many modern languages use similar punctuation symbols for marking sentence or subsentence and anyway we need to know given language alphabet if we want proceed, so we can treat everything else as a punctuation mark.

  1. Alignment

We want to match a given sequence of speeches in a form of time intervals to sentences in a form of sequence of words.

Given:
S=lbrace [s_i, e_i] rbrace	– time intervals
T = [[w_1, ...], ... ]	– sequence of sequences of words

First we need create a method for estimating time of speaking given sentence.
A simple approach to this problem is to estimate a time to say a single character and use it to estimate time for whole sentence.

E(size 10 {time of single character}) = {sum_{W} sum_{w in W} lline w rline } over {sum_{lline s_i, e_i rline in S} (e_i - s_i)}

E(size 10 {time of word} w) = sum_{c in w} E(size 10 {time of single character})

We would like to minimize the difference of the estimated time and speech time:

This problem is easily solve with dynamic programming.

We iterate over speeches.

5. Audio based alignment.

  1. Grapheme to phoneme conversion grammar.

For the purpose of speech recognition we require very accurate dictionaries of each trained word and its phonetic represantation.
Although we are dealing here with a slightly easier problem and only an aproximation of phonetic description can be used. My proposal is to use a conversion grammar, which assigns a sequence of phonemes to given sequence of graphemes.
The idea behind is, that we don't really want to distinguish certain words and we can merge similar phones in single phoneme and use only one of that. It will work as far as we still can distinguish each phones in a any given word. Which means, that our phonetic conversion must have the same amount of phonemes as there are distinguished phones and each used phoneme should stand out from the neighboring phonemes.

It seems, that for polish language it works well enough.

  1. Differences between english, russian and polish phonetics

  1. Similar language audio model alignment.

Bibliography

1. Houghton Mifflin Company. The American Heritage Dictionary of the English Language, Fourth Edition, 2000.
2. Prof. W. Alberti. The anatomy and physiology of the ear and hearing.
3. Prof. Joseph Picone Fundamentals of speech recognition
4. Olson Harry F. (1967) Music, Physics and Engineering
5. Stevens Stanly Smith, Volkman John, Newman Edwin B. (1937) A scale for the measurement of the psychological magnitude pitch Journal of the Acoustical Society of America
6. Douglas O'Shaughnessy (1987) Speech communication: human and machine.
7. Zwicker E. (1961) Subdivision of the audible frequency range into critical bands.
8. H.P. Combrinck and E.C. Botha On The Mel-scaled Cepstrum
9. Welch P. (1967) The use of fast Fourier Transform for the estimation of power spectra: A method based on time averaging over short, modified periodograms
10. Steven W. Smith The scientist and engineer's guide to digital signal processing.
11. Mark A. Pinsky Introduction to Fourier analysis and wavelets